INSTALLATION INSTRUCTIONS						PI-083

H.D. Fuse Holder for 240 Series 1982-89				          Part # 3E0240

Thank you for purchasing ipd’s H.D. waterproof fuse holder assembly. The factory fuse holder allowed water and engine compartment fumes to seep in and corrode the connection. This caused an array of electrical problems from intermittent starting and stalling, to no start conditions. One popular Volvo repair shop credited this part as the #1 cause of no start tow-ins to his shop! After hearing of repeated stories about all the unusual, inconsistent and costly  problems that this little inexpensive part caused, we did a little research and found this quality solution.

Please read through the instructions before attempting installation. If you are not comfortable with the terms or procedures mentioned here, or you feel this may be beyond your technical expertise, have this professionally installed.

TOOLS NEEDED

Wire cutters, solderless connector crimping tool (found on most wire strippers) and a heat gun (a good hair blow dryer, on the high heat setting, will sometimes work).

CAUTION - disconnect the negative battery cable before starting!

You’ll find the fuse holder under the hood located on the driver side inner fender of the car. The easiest way to find it is by following the smaller of the 2 red wires connected to the positive (+) battery post. Follow this smaller red wire about a foot back and it will lead you to the original fuse holder. The original holder is held in place by a small metal clip that attaches it to a metal mounting bracket. Pull up on the holder and it should come free, be careful to not lose the metal clip as it will be needed to hold the new assembly in place. Depending on the year of your car, you may have to pull the assembly out from under the power steering fluid reservoir to allow good access to the wires.

1. Approximate the position of the new holder to determine where to cut the old wires. Be conservative and leave a little extra of the old wire as it won’t hurt to be a little long, but cutting them too short will cause mounting problems.

2. Clean the old wire a few inches back and carefully strip off about  1/4” of insulation and crimp one end of the wire connectors to each of the old wires.  Strip 1/4” of insulation from the new wires, slide the supplied heat shrink tubing over the new wires before making the final crimps to the new wires. Make sure the crimping is strong by pulling on it firmly.

3. Now slide the heat shrink tubing over the wire connectors and use a heat gun or hair dryer to activate the heat shrink. If you have never used heat shrink before, it shrinks down under the application of heat to ensure a water tight connection. If you do not have a heat gun or hair dryer powerful enough to activate (make it shrink) the heat shrink tubing, we suggest postponing this step until you can borrow a heat gun or have a service station or your mechanic do this later. In the short term it won’t cause a problem to wait.

CAUTION - DO NOT use a flame or lighter as the battery gives off explosive hydrogen fumes and could explode.

4. To finish the installation, use the original metal clip to attach the new holder in the original location.

5. Reattach the negative battery cable.

Limited One Year Warranty

ipd warrants to the original purchaser that the parts manufactured and/or sold by ipd (the Product) is free from defects in material and workmanship under normal use. ipd warrants that the Product will perform substantially in accordance with the specifications set forth in the documentation provided with it. The above express warranties are made for a period of the lesser of 12,000 miles or 12 months from the date the Product is installed in your vehicle.

Any improper use, operation beyond capacity, substitution of parts not approved by ipd in writing, any alteration or repair by others, or any removal, defacing or altering of the identification shall void this warranty. There is no warranty on high-performance or race related parts due to the nature of usage.

The purchaser shall notify ipd at 1-800-444-6473 of any defect within the warranty period no later than thirty (30) days after purchaser discovers the defect. Should any failure to conform to this warranty appear within the warranty period, ipd shall, on notification, correct the nonconformity at its option, either by repairing any defective part, or by making available, FOB ipd’s plant, a repaired or replacement part. The purchaser must insure any defective item being returned because ipd does not assume risk of loss or damage while in transit. No payment or reimbursement shall be made for installation, removal, transportation or other charges. The remedies set forth in this instrument are exclusive, and the liability of ipd with respect to any sale shall not exceed the price of the Product on which the liability is based.

EXCEPT AS STATED OTHERWISE IN THIS WARRANTY, ipd MAKES NO WARRANTIES, EXPRESS OR IMPLIED, INCLUDING WITHOUT LIMITATION, ANY WARRANTY OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE. Some states do not allow limitations on how long an implied warranty lasts, so the above limitation may not apply to you. ipd shall not in any case be liable for special, incidental, consequential, indirect, or other similar damages arising from any breach of these warranties even if ipd or its agent has been advised of the possibility of such damages. Some states do not allow the exclusion or limitation of incidental or consequential damages so the above limitation or exclusion may not apply to you.

This warranty is governed by the laws of the State of Oregon.

Component List

Part #	Description	Qty.

1FH240	Fuse Holder	1

254131	Heat Shrink Tube	2

423005	Connector, Butt	2

As always, we invite your input to these instructions or ways to improve this product and to make it simpler for the next person. 1-800-444-6473   THANKS!